Instruction sheet—LEEMC LCD step motorized lift

Model number: LCD85-3C

1,Specification

1-1,Exterior dimension:

D:870mm

W:500mm

H:850mm

1-2, spare parts:

Remark:A:Please use the spare parts from our factory ,in order to avoid any accident please don’t use any other spare parts without approval.

B:Please check all the spare parts, please contact us if any losing and damage.

1-3,install tooling(factory not supply)

2,electric specification

2-1 ,Input voltage ,output current

A: input voltage/current/frequency: 100-240V,AC

B: output current: DC240V,3A

  - Motor

| Type | Voltage | No-load current | Load current | Temperature |
| --- | --- | --- | --- | --- |
| DN3435-3046 | DC24V | ≤0.5A | ≤1.5A | -20℃~50℃ |
| PR545AG-12300-IG32-721 | DC24V | ≤0.3A | ≤0.5A | -20℃~50℃ |

3，Installation

3-1,Make sure the wall is firm enough to be mounted this product. Make the note on the ceiling by the pencil, use the percussive drilling to make the holes :depth :75mm,long:10mm.Put the 9pcs screws⑥ to the holes.(photo1 )

3-2,Take away 8pcs screws,2 people lift and install the main part,and mount the the top plate. Connect the power.(photo2)

3-3,Insert the square tube to the plate by 2pcs ⑦ screws. Install the TV mounts on the two sides of the tubes. Adjust the position based on the holes on the back side of the TV by the 4pcs ⑦ screws. Press the button “on” in the remote controller to let the product down.(photo3)

3-4,Install screws ① &② to the back side of the TV. Then mount the TV to the plate.(photo 4)

3-5,Use the screws③④⑤to tighten the TV and the mount. Put the cable of the TV to the wire cleat.( photo 5)

4-2,connectors:

A: connectors on the top side of the unit: power input/video input/audio input/TV signal input. Connect those inputs into the TV on the bracket. Please don’t connect to the TV directly.

B :connectors on the bottom side of the unit: power /video output/audio output/TV signal

5,Paremeter:

|  | Fit for LCD(inch) | Exterior Size(mm) | Install max size(mm) | Install min size(mm) | Load capacity(kg) | Left/right angel | Up/dowm angel | Net W(kg) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| LCD85-3C | 46-50 | 870*500*850 | 830*450 | 600*300 | 50 | ±35 | 0-87 | 34.3±10 |

6,Remark: